## Slide 1: BGS ARPIT (Amateur Radio Payload for Information Transmission) Electrical Interface Details Power, TM(RS485), TC & RF
SJC INSTITUTE OF TECHNOLOGY

## Slide 2
ID | Parameter | Unit | Specification
1. | Payload electrical interface | - | On Payload: Part Number: IM24308/3-1F-ND Manufacturer: ITT Cannon, LLC Description:9 Position D-Sub Plug, Male Pins Connector From Platform: The expected connection is a female DB9 D-sub connector (9 Pin)
2. | Power requirement from PS4-OP | - | Peak (Tx mode): 7 W Standby (Rx mode): 0.5 W
Figure: Block Diagram of the Payload
Power Consumption
Pin 1 | RBLIVE
Pin 2 | NC
Pin 3 | NC
Pin 4 | NC
Pin 5 | RBRETURN
Pin 6 | NC
Pin 7 | NC
Pin 8 | NC
Pin 9 | SGRP
RS485 - NO
TC - NO
RF - YES
Energy Storage(battery) - NO
Duration of operation – 7 days initially to evaluate the in-orbit performance of the payload. As this is a payload meant to provide continuous global APRS transponder services to the amateur radio users, we request the authority to keep it ON till the end the POEM mission.

## Slide 3: Power convertor circuit diagram
Vin PIN 1 of DB 9 connector
GND PIN 5 of DB 9 connector
Figure: Interface with Power
Figure: Interface with OBC of PSLV
NOTE: No on-board energy/cells/batteries are used in the payload.
Source: https://www.ti.com/lit/ug/snvu680/snvu680.pdf
TM/TC and other parameters are communicated with the payload using APRS packets over payload frequencies

## Slide 4
  Galvanic Isolation:
  We have used an isolated DC/DC Converter with short circuit protection and EMI filter.
  The LM25184-Q1 42-VIN PSR Flyback DC/DC Converter provides functional grade isolation to 1500 V DC. [1]
  Short Circuit Protection: Over Current Protection triggers at 4.1 A.
  In case of an overcurrent condition on the isolated output or outputs, the output voltage drops lower than the regulation level since the maximum power delivered is limited by the peak current capability on the primary side. The peak primary current is maintained at 4.1 A (plus an amount related to the 100-ns propagation delay of the current limit comparator) until the output decreases to the secondary diode voltage drop to impact the reflected signal on the primary side. At this point, the LM25184-Q1 assumes the output cannot be recovered and re-calibrates its switching frequency to 9 kHz until the overload condition is removed. The LM25184-Q1 responds with similar behavior to an output short circuit condition. [2]
  Inrush current measurement – Will be updated later
  Pre EMI/EMC checks done if any – Only Bench test and Functionality test completed.
  Ensure electrolytic capacitors are not used – No electrolytic capacitors are used.
[1]https://www.ti.com/lit/ug/snvu680/snvu680.pdf –Datasheet of the DC- DC Converter
[2] https://www.ti.com/lit/gpn/lm25184-q1 - Datasheet of the IC used in the DC-DC Converter

## Slide 5: RS485 circuit and highlights of test done at VSSC (18th-22nd March24 or IN-SPACe)
The Payload does not have any RS485 circuit.
The testing at VSSC is yet to be done.

## Slide 6: RF details if any or details of analog/digital channel interface
Parameters | Units | Values
Parameters to be measured | - | NA (Power (28V to 42V) with ON/OFF capability with ON/OFF status TM) TM/TC and other parameters are communicated with the payload using APRS packets over payload frequencies) Data Rate: 1200 bps
TM/TC | - | 
Data Rates | - | 
Frequency of operation | MHz | 145.825 (APRS - Digipeater Telemetry Packet) 145.870 Other modes (Voice, SSTV)
Baud Rate |  | 1200
Duty Cycle |  | 67%
Transmit power | W | 2
FM Frequency deviation | Hz | 2500
RF Modulation |  | FM
Message types |  | Audio, Text, Image
Baseband Modulation | Audio | None, sampled and quantized audio
 | Text | AFSK modulation, AX.25 Frame Format
 | Image | SSTV PD120 and Robot72 Modes
  Payload RF configuration
Figure: AX.25 Frame Format

## Slide 7
Sl. No | Comments | Action
1 | MAX3443 to be used in all payload without extra protections like TVS diodes for RS485 links | Not Applicable
2 | Fuse rating and DC-DC converter data-sheets to be submitted | Explicitly mentioned in slide 4
3 | Male connectors to be used used at payload end especially for power connectors and type of connection to be specified like crimped or soldered. | Male DSUB 9 Pin ITT Connector MIL Grade IM24308/3-1F-ND has been used. Connection type: Soldered
4 | Inrush current to be measured and updated in documents | Will be measured and updated.
5 | Justification on high value input filter capacitor (as it may rise inrush currents) | Not applicable
6 | Grade of components to be specified (Industrial, Automotive, Mil, Space etc.) | DSUB 9 Pin Connector – MIL Grade Rest of the components - Industrial
7 | Part nos and part values to be shown on circuit diagrams (if not already done) | Taken care
8 | TM packets details to be shared | TM is communicated with the payload using APRS packets over payload frequencies. APRS AX.25 Standard Packet format is mentioned in slide 6.
9 | Mission operation detailed plan to be shared | Once the Payload is switched ON, it acts as a “Digipeater” and sends information and TM via APRS over payload frequencies till the end of mission.
10 | RS485 checks report to be submitted (if not done) | Not applicable
11 | Isolated DC-DC converters are compulsory for all payloads | We have isolated DC-DC Converter.